## Slide 1
Computation of Mutual Information Metric for Image Registration on Multiple GPUs
Andrew V. Adinetz1, Markus Axer2, Marcel Huysegoms2, Stefan Köhnen2, Jiri Kraus3, Dirk Pleiter1
26.08.2013
1 JSC, Forschungszentrum Jülich
2 INM-1, Forschungszentrum Jülich
3 NVIDIA GmbH

## Slide 2
Brain Image Registration
Multi-GPU Implementation
  system memory
  listupdate
Performance Evaluation
Conclusion
Outline

## Slide 3
Preparation of the brain

## Slide 4
BigBrain – first high-resolution brain model at microscopical scale
7404 histological sections stained for cell bodies
scanned with a flad bed scanner
original resolution 10 × 10 × 20 μm3 (11.000 × 13.000 pixels)
downscaling to 20 μm isotropic
removal of artifacts
1 Terabyte
in cooperation with Alan Evans, McGill, Montreal
Amunts et al. (2013) Science
Pushing the limits for a cellular brain model
Notes: 6 years

## Slide 8
The process of aligning images is called registration
Image Registration
ITK Workflow

## Slide 9
i, j – pixel values (0 .. 255)
successful for multi-modal registration
Mutual Information Metric

## Slide 10
main computational kernel
transform can be complex (1000+ parameters)
GPU implementation: 1 pixel/thread, atomics
Two Image Cross-Histogram
for(int y = 0; y < fixed_sz_y; y++)
for(int x = 0; x < fixed_sz_x; x++) {
int i = bin(fixed[x, y]);
float x1 = transform_x(x, y);
float y1 = transform_y(x, y);
int j = bin(interpolate(moving, x1, y1));
histogram[i, j]++; // atomic on GPU
}

## Slide 11
Large Data Size
size: 3.000 × 3.000 px
pixel size: 60 × 60 μm
file size: 30 MB
Large-area Polarimeter
size: 100.000 × 100.000 px
pixel size: 1.6 x 1.6 μm
file size: 40 GB
Polarizing Microscope

## Slide 12
Domain decomposition
  distribute fixed and moving images
  histogram contributions summed up
Moving image: how to handle?
  irregular access pattern
Approaches
  System memory replication (sysmem)
  Listupdate (listupdate)
Multi-GPU Mutual Information

## Slide 13
Replicate entire moving image in pinned host RAM
  accessible to GPU
+ easy to implement
– system memory accesses are slower
– cannot use texture interpolation
Optimizations
  moving image halo in GPU RAM
System Memory Replication

## Slide 14
Processing
  buffer remote accesses
  exchange buffers
  compute contributions remotely
+ computation-communication overlap
– hard to implement
– chunk processing (or won‘t fit into buffer)
Optimizations
  buffers: AoS vs. SoA, atomics vs. grouping
  using multiple streams
Listupdate
typedef struct {
float[2] movingCoords;
short destRank;
char fixedBin;
} message_t;

## Slide 15
Chunk Processing and Overlap
Process chunk
Group
Exchange
Handle messages
Process chunk
Group
Exchange
Process chunk
Group
1
2
Fixed Image
Fixed Image
y
x
(0,0)

## Slide 16
atomics
  each writing thread increments atomic counter
  + simpler
  – atomics can be a bottleneck
  – one buffer per receiver required
grouping
  each thread writes to fixed location
  buffers grouped before sending
  + single buffer, less memory
  + optimized grouping (shared-memory atomics, prefix sum)
  – more complicated (separate kernel required)
Buffer Writeout: Atomics vs. Group

## Slide 17
Benchmark setup
Fixed Image
Fixed Image
y
Moving Image
x
(0,0)
Remote access
Mask

## Slide 18
JUDGE
  256-node GPU cluster
  Each M2070 node:
    2x M2070 (Fermi) GPU, each 6 GB RAM
    12-core X5650 CPU @ 2.67 GHz, 96 GB RAM
JuHydra
  single-node Kepler machine
    2x K20X (Kepler) GPU, each 6 GB RAM
    16-core E5-2650 CPU @ 2 GHz, 64 GB RAM
Test Hardware

## Slide 19
Baseline: Full Replication (M2070)
Chart: Rotation angle
ideal scalability

## Slide 20
Sysmem on Fermi
Chart: Rotation angle

## Slide 21
Sysmem on Fermi: Explanation
No sysmem Access
Good Coalescing
Few sysmem Access
Bad Coalescing
Many sysmem Access
Bad Coalescing
Most sysmem Access
Good Coalescing

## Slide 22
Sysmem on Fermi: PCI-E Queries
Chart: Rotation angle

## Slide 23
Sysmem: Halo Sizes
Chart: Angle, degrees
| 0.0 | 1.8 | 3.6 | 5.4 | 7.2 | 9.0 | 10.8 | 12.6 | 14.4 | 16.2 | 18.0 | 19.8 | 21.6 | 23.40000000000001 | 25.20000000000001 | 27.00000000000001 | 28.80000000000001 | 30.60000000000001 | 32.40000000000001 | 34.2 | 36.0 | 37.8 | 39.6 | 41.4 | 43.19999999999998 | 44.99999999999998 | 46.79999999999998 | 48.59999999999998 | 50.39999999999997 | 52.19999999999998 | 53.99999999999997 | 55.79999999999996 | 57.59999999999996 | 59.39999999999996 | 61.19999999999996 | 62.99999999999995 | 64.79999999999996 | 66.59999999999996 | 68.39999999999994 | 70.19999999999994 | 71.99999999999998 | 73.79999999999996 | 75.59999999999993 | 77.39999999999993 | 79.19999999999993 | 80.99999999999992 | 82.79999999999992 | 84.59999999999992 | 86.39999999999992 | 88.19999999999991 | 89.9999999999999 | 91.7999999999999 | 93.5999999999999 | 95.3999999999999 | 97.1999999999999 | 98.9999999999999 | 100.8 | 102.6 | 104.4 | 106.2 | 108.0 | 109.8 | 111.6 | 113.4 | 115.2 | 117.0 | 118.8 | 120.6 | 122.4 | 124.2 | 126.0 | 127.8 | 129.6 | 131.4 | 133.2 | 135.0 | 136.7999999999999 | 138.6 | 140.4 | 142.2 | 144.0 | 145.8 | 147.6 | 149.4 | 151.2 | 153.0 | 154.8 | 156.6 | 158.4 | 160.2 | 162.0000000000001 | 163.8000000000001 | 165.6000000000001 | 167.4000000000001 | 169.2000000000001 | 171.0000000000001 | 172.8000000000001 | 174.6000000000001 | 176.4000000000001 | 178.2000000000002 | 180.0000000000002
2 K20X, baseline | 0.025071 | 0.026017 | 0.026238 | 0.026334 | 0.026189 | 0.025992 | 0.02589 | 0.025884 | 0.025699 | 0.025635 | 0.025632 | 0.025695 | 0.025808 | 0.025931 | 0.026085 | 0.026171 | 0.026311 | 0.026399 | 0.026507 | 0.026562 | 0.026615
2 K20X, sysmem | 0.02705 | 0.038492 | 0.050658 | 0.062836 | 0.075975 | 0.091562 | 0.11027 | 0.13218 | 0.15608 | 0.18246 | 0.21193 | 0.24357 | 0.27798 | 0.31524 | 0.35635 | 0.40137 | 0.44987 | 0.5039 | 0.56246 | 0.6266 | 0.69389
2 K20X, 5% halo | 0.027118 | 0.028592 | 0.03924 | 0.051226 | 0.0636 | 0.079859 | 0.097397 | 0.11769 | 0.14025 | 0.16504 | 0.19186 | 0.22248 | 0.2551 | 0.28959 | 0.32891 | 0.37156 | 0.41856 | 0.47192 | 0.52936 | 0.59078 | 0.65843
2 K20X, 10% halo | 0.027135 | 0.026382 | 0.030809 | 0.040593 | 0.05251 | 0.066435 | 0.082037 | 0.10033 | 0.12036 | 0.14354 | 0.16843 | 0.1971 | 0.22723 | 0.26087 | 0.29697 | 0.33716 | 0.38062 | 0.4284 | 0.48126 | 0.53804 | 0.59833
2 K20X, 15% halo | 0.027188 | 0.026413 | 0.026626 | 0.032763 | 0.042605 | 0.054825 | 0.069821 | 0.086701 | 0.10533 | 0.12636 | 0.14915 | 0.17524 | 0.20492 | 0.23597 | 0.27081 | 0.30889 | 0.34902 | 0.39373 | 0.44364 | 0.49658 | 0.5547
2 K20X, 20% halo | 0.027155 | 0.026415 | 0.026355 | 0.02792 | 0.034969 | 0.045033 | 0.058671 | 0.074102 | 0.091291 | 0.11109 | 0.13256 | 0.15626 | 0.18303 | 0.21296 | 0.24493 | 0.28025 | 0.31879 | 0.36108 | 0.40728 | 0.45749 | 0.51272
2 K20X, 25% halo | 0.027151 | 0.026406 | 0.026395 | 0.026214 | 0.029659 | 0.037316 | 0.048417 | 0.063674 | 0.080042 | 0.099228 | 0.1212 | 0.14335 | 0.16804 | 0.19525 | 0.22525 | 0.25948 | 0.29569 | 0.33855 | 0.38092 | 0.42953 | 0.48384
mostly quantitative, not qualitative difference

## Slide 24
Listupdate: Multiple Streams
4 streams look the best
Chart: Angle, degrees

## Slide 25
Listupdate: AoS vs SoA, Atomics vs Group
SoA + atomics looks best
Chart: Angle, degrees

## Slide 26
Sysmem vs. Listupdate: Fermi
Chart: Angle, degrees
on Fermi, sysmem is better

## Slide 27
Sysmem vs. Listupdate: Kepler (Closeup)
Chart: Angle, degrees
| 0.0 | 1.8 | 3.6 | 5.4 | 7.2 | 9.0 | 10.8 | 12.6 | 14.4 | 16.2 | 18.0 | 19.8 | 21.6 | 23.40000000000001 | 25.20000000000001 | 27.00000000000001 | 28.80000000000001 | 30.60000000000001 | 32.40000000000001 | 34.2 | 36.0 | 37.8 | 39.6 | 41.4 | 43.19999999999998 | 44.99999999999998 | 46.79999999999998 | 48.59999999999998 | 50.39999999999997 | 52.19999999999998 | 53.99999999999997 | 55.79999999999996 | 57.59999999999996 | 59.39999999999996 | 61.19999999999996 | 62.99999999999995 | 64.79999999999996 | 66.59999999999996 | 68.39999999999994 | 70.19999999999994 | 71.99999999999998 | 73.79999999999996 | 75.59999999999993 | 77.39999999999993 | 79.19999999999993 | 80.99999999999992 | 82.79999999999992 | 84.59999999999992 | 86.39999999999992 | 88.19999999999991 | 89.9999999999999 | 91.7999999999999 | 93.5999999999999 | 95.3999999999999 | 97.1999999999999 | 98.9999999999999 | 100.8 | 102.6 | 104.4 | 106.2 | 108.0 | 109.8 | 111.6 | 113.4 | 115.2 | 117.0 | 118.8 | 120.6 | 122.4 | 124.2 | 126.0 | 127.8 | 129.6 | 131.4 | 133.2 | 135.0 | 136.7999999999999 | 138.6 | 140.4 | 142.2 | 144.0 | 145.8 | 147.6 | 149.4 | 151.2 | 153.0 | 154.8 | 156.6 | 158.4 | 160.2 | 162.0000000000001 | 163.8000000000001 | 165.6000000000001 | 167.4000000000001 | 169.2000000000001 | 171.0000000000001 | 172.8000000000001 | 174.6000000000001 | 176.4000000000001 | 178.2000000000002 | 180.0000000000002
2 K20X, SoA | 0.03922 | 0.039138 | 0.043321 | 0.048419 | 0.053414 | 0.059487 | 0.06605 | 0.071178 | 0.077579 | 0.084375 | 0.091172 | 0.095993 | 0.10025 | 0.10867 | 0.11399 | 0.12316 | 0.12689 | 0.13179 | 0.13519 | 0.14415 | 0.14833
2 K20X, baseline | 0.025071 | 0.026017 | 0.026238 | 0.026334 | 0.026189 | 0.025992 | 0.02589 | 0.025884 | 0.025699 | 0.025635 | 0.025632 | 0.025695 | 0.025808 | 0.025931 | 0.026085 | 0.026171 | 0.026311 | 0.026399 | 0.026507 | 0.026562 | 0.026615
2 K20X, sysmem | 0.02705 | 0.038492 | 0.050658 | 0.062836 | 0.075975 | 0.091562 | 0.11027 | 0.13218 | 0.15608 | 0.18246 | 0.21193 | 0.24357 | 0.27798 | 0.31524 | 0.35635 | 0.40137 | 0.44987 | 0.5039 | 0.56246 | 0.6266 | 0.69389
2 K20X, 25% halo | 0.027151 | 0.026406 | 0.026395 | 0.026214 | 0.029659 | 0.037316 | 0.048417 | 0.063674 | 0.080042 | 0.099228 | 0.1212 | 0.14335 | 0.16804 | 0.19525 | 0.22525 | 0.25948 | 0.29569 | 0.33855 | 0.38092 | 0.42953 | 0.48384
on Kepler, listupdate is better

## Slide 28
Fermi
  performance limited by atomics
  system memory replication is better
Kepler
  order of magnitude faster than Fermi
  no longer dominated by atomics
  listupdate (atomic, SoA, 4 streams) is better
Future work
  Compression
  Trials on real images
Conclusions

## Slide 29
INM-1 at FZJ: http://www.fz-juelich.de/inm/inm-1/EN/Home/home_node.html
NVidia Application Lab at FZJ: http://www.fz-juelich.de/ias/jsc/nvlab
  Andrew V. Adinetz: adinetz@gmail.com
  Jiri Kraus: jkraus@nvidia.com
  Dirk Pleiter: d.pleiter@fz-juelich.de
Questions
?